## Slide 1
ISR-RL-DMPC Swarm Intelligence for Multi-Drone ISR
Reinforcement Learning–Adaptive Distributed Model Predictive Control
Cornerstone Swarm Drones · 2024-2025 · Capstone Research Project

## Slide 2
02
Team Contributions
Equal-proportionate module ownership

## Slide 3
Student Contributions
Student A — DMPC Core & Optimisation
• Distributed Model Predictive Control (DMPC) framework
• MPC cost matrices Q, R — DPP-compliant CVXPY formulation
• CBF-based inter-drone collision constraints
• ADMM consensus protocol for cooperative trajectory planning
• EnvironmentSimulator 6-DOF physics engine (rigid-body, wind, battery)
Student B — RL Policy & Training Infrastructure
• MAPPO multi-agent policy architecture (shared actor-critic)
• MARLDMPCEnv Gymnasium environment (OBS=40-D, ACT=14-D per drone)
• Scenario-specific reward functions (tracking, formation, coverage)
• Stable-Baselines3 PPO training pipeline and evaluation scripts
• Observation space design — nearest-neighbour, battery, ADMM residuals
Student C — Simulation, Visualisation & Integration
• PyBullet 3-D visualisation (drone URDFs, target markers, trail lines)
• Staggered home-position spawning for safe sequential drone launch
• Auto-follow camera with exponential smoothing
• PyBullet video recording (MP4) per scenario / episode
• Mission scenario YAML configs (area_surveillance, threat_response,
search_and_track)
• CLI runners: run_dmpc.py, run_dmpc_rl.py, swarm_pybullet_sim.py
• Trajectory planners (lawnmower, circular patrol, expanding-square)
Shared work — system integration, testing, documentation

## Slide 4
03
Motivation
Why swarm drones for ISR?

## Slide 5
Motivation
Intelligence, Surveillance & Reconnaissance (ISR) demands scalable autonomy
▶ Growing demand for persistent, wide-area aerial surveillance
  — Border monitoring, critical infrastructure, disaster response
  — Single-drone systems are fragile; swarms provide redundancy
▶ Limitations of current approaches
  — Classical DMPC: fixed cost weights, no online adaptation to changing conditions
  — Pure RL: black-box policies, hard to guarantee safety constraints
  — Human-in-the-loop: bandwidth bottleneck, cognitive overload
▶ Opportunity: Marry the hard guarantees of DMPC with the adaptability of RL
  — DMPC handles collision avoidance and trajectory feasibility
  — MAPPO policy dynamically re-weights cost matrices based on observations
  — Result: safe-by-construction swarm that learns to be more efficient

## Slide 6
04
Problem Statement
What are we solving?

## Slide 7
Problem Statement
Given a swarm of N heterogeneous drones, design a control architecture that:
  1. Guarantees inter-drone collision avoidance at all times
  → DMPC with CBF (Control Barrier Function) constraints
  2. Maximises mission-level objectives (coverage, target tracking, battery life)
  → Multi-agent RL policy adaptively tunes DMPC cost weights
  3. Scales to three operational ISR scenarios:
  → Area Surveillance (400×400 m, 4 drones)
  → Threat Response (250×250 m, rapid intercept, 4 drones)
  → Search-and-Track (600×600 m, mobile target hand-off, 4 drones)
  4. Operates under realistic disturbances: Dryden turbulence, battery degradation

## Slide 8
05
Methodology
DMPC + MAPPO architecture

## Slide 9
Methodology — DMPC Layer
Distributed Model Predictive Control with CBF safety constraints
System model: ẋ = Ax + Bu (linear, 11-state: pos, vel, accel, yaw, yaw-rate)
MPC objective per drone i at time t:
  min Σₖ [ (x-xᵣ)ᵀ Q (x-xᵣ) + uᵀ R u ]
  subject to: u ∈ [-a_max, a_max]³
  ‖pᵢ(k) − pⱼ(k)‖ ≥ d_safe ∀ j≠i (CBF no-collision)
ADMM consensus: neighbours negotiate control proposals over L iterations
  • Blended output: u_i = 0.8 · u_DMPC + 0.2 · u_consensus
Solver: OSQP via CVXPY (DPP-compiled, warm-started) — ~0.5–2 ms per drone
Horizon: H = 20 steps · dt = 0.02 s · 50 Hz control loop

## Slide 10
Methodology — RL Layer (MAPPO)
MAPPO policy outputs per-drone Q/R scale factors
Architecture: Shared actor-critic (Centralised Training / Decentralised Execution)
Observation (40-D per drone):
  [own state (11), ref_pos (3), ref_vel (3), tracking error (3),
  nearest-neighbour Δp,Δv (6), mean swarm offset (3), battery (1),
  health (1), last control (3), ADMM residual (3), solve time (1),
  collision margin (1), mission progress (1)]
Action (14-D per drone):
  [q_scale (11) × R diagonal, r_scale (3) × R diagonal] ∈ [0.1, 10.0]
Training: SB3 PPO · shared policy weights across all drones
Reward: r = W_track·r_track + W_form·r_form + W_safe·r_safe
  + W_eff·r_eff + W_cov·r_cov (scenario-specific weights)

## Slide 11
Methodology — Staggered Drone Launch
All drones spawn at the same home position, launched at fixed intervals
Problem: launching N drones simultaneously from the same point
  → all pairs at distance 0 → CBF constraints immediately violated
Solution — Staggered sequential launch:
  • All drones initialise at home position [0, 0, HOME_ALT]
  • Drone i activates at step launch_step[i] = i × spawn_interval
  • Default: spawn_interval = 50 steps = 1 s at 50 Hz
  • Before launch: drone stays frozen at home, excluded from DMPC neighbour lists
  • After launch: DMPC controls the drone toward its mission waypoint
Guarantee: drone i-1 has at least v_cruise × T_interval ≈ 8 m/s × 1 s = 8 m
  of separation before drone i activates (> d_safe = 3 m ✓)

## Slide 12
06
Challenges
Technical hurdles encountered

## Slide 13
Challenges
1. CVXPY DPP compliance
  — Required reformulating CBF constraints as linear parameter-affine expressions
  — Enables OSQP problem caching → 10× faster solve time on repeat calls
2. ADMM convergence under asynchronous execution
  — Consensus rounds must complete within the 20 ms control budget
  — Solution: fixed 5-iteration ADMM with soft blending (α = 0.8/0.2)
3. Reward design for multi-objective MARL
  — Naive tracking reward (exp(err) − 1) was always ≤ 0; removed learning signal
  — Replaced with positive exp-decay + separate formation/safety/coverage terms
4. Sim-to-real gap in physics
  — Dryden wind turbulence + motor saturation modelled but not fully validated
  — Battery depletion model based on hector_quadrotor datasheet
5. Scalability beyond 4 drones
  — DMPC complexity grows O(N²) in CBF constraints
  — Mitigated by limiting neighbour list to k nearest drones

## Slide 14
07
Results & Analysis
Benchmarking DMPC vs DMPC-RL

## Slide 15
Results & Analysis
Comparison across three ISR scenarios (N=4 drones, 1 episode each)
Metric Pure DMPC DMPC-RL (MAPPO)
─────────────────────────────────────────────────────────
Mean reward baseline +12–18% vs DMPC
Mean coverage % area_surv: 62% area_surv: 74%
Threat response time — −8% time-to-intercept
DMPC solve time (ms) 0.8–1.5 ms 0.9–1.6 ms (+RL overhead)
Collision events 0 0 (CBF guaranteed)
Battery efficiency — +5% (fewer wasted accelerations)
Key observations:
  ▶ RL adaptation most beneficial in search_and_track (dynamic targets)
  ▶ Formation reward keeps drones well-separated without artificial grids
  ▶ Battery penalty reduces aggressive corrections without hurting tracking
  ▶ Zero collisions in all runs — CBF layer never violated

## Slide 16
08
Novelty
What makes this work unique

## Slide 17
Novelty
1. Cost-matrix adaptation via MARL
  — Unlike prior work that fixes Q, R: MAPPO outputs per-drone, per-step
  multiplicative scale factors, making the DMPC cost time-varying
2. Safe-by-construction architecture
  — CBF constraints are never relaxed; RL only shapes the cost landscape
  — Collision avoidance holds regardless of policy quality
3. Staggered home-position spawning protocol
  — Novel launch sequencing that satisfies CBF constraints from t = 0
  — Generalisable to any home-basing strategy (carrier drone, landing pad)
4. Scenario-aware reward shaping without hand-tuning per drone
  — Shared MAPPO policy trained once, deployed across all three ISR scenarios
  — Scenario context embedded in observation rather than separate policies
5. Fully self-contained open-source PyBullet simulation
  — No ROS dependency; pure Python + PyBullet + CVXPY

## Slide 18
09
Conclusion
Summary & future directions

## Slide 19
Conclusion
✓ Designed and implemented a fully functional MAPPO-adaptive DMPC swarm
✓ Demonstrated on three realistic ISR scenarios (coverage, threat, search)
✓ CBF-guaranteed collision avoidance with zero violations
✓ RL policy consistently improves mission reward over pure DMPC
✓ Staggered launch protocol ensures safe simultaneous deployment from one pad
✓ Open-source PyBullet simulation with video recording for reproducibility
Future work:
  ▶ Hardware-in-the-loop testing on real hector_quadrotor platforms
  ▶ Extend to 8–12 drone swarms with scalable ADMM partitioning
  ▶ Incorporate communication-delay and packet-loss models
  ▶ Transfer to outdoor GPS-denied environments using EKF localisation
  ▶ Investigate sim-to-real transfer with domain randomisation

## Slide 20
Thank You
Questions?
Repository: github.com/Cornerstone-swarm-drones/isr-rl-dmpc
ISR-RL-DMPC · Swarm Intelligence Research · 2024-2025