## Slide 1
ISR-RL-DMPC
Autonomous Multi-Drone ISR Swarm using MARL-Adaptive DMPC + ADMM
Cornerstone Presentation
Team: Jivesh Kesar • Harsh • Rohit Shankar Sinha
Repository: Cornerstone-swarm-drones/isr-rl-dmpc
ISR-RL-DMPC • Cornerstone Project

## Slide 2
Agenda
1) Motivation
2) Problem Statement
3) Methodology (module-wise deep dive)
4) Challenges
5) Results and Analysis
6) Novelty
7) Conclusion
ISR-RL-DMPC • Cornerstone Project

## Slide 3
01 • Motivation
Why this project?
Operational Need
Research Gap
• ISR missions require fast area coverage and persistent tracking.
• Single-drone systems are fragile and coverage-limited.
• Swarms improve redundancy, responsiveness, and spatial diversity.
• Real-time autonomy is needed under uncertainty and constraints.
• Pure RL lacks hard safety guarantees in mission-critical loops.
• Classical DMPC with fixed Q/R is not adaptive across contexts.
• Need adaptive control priorities with convex optimization safety.
• Need distributed consensus for coherent multi-drone behavior.
ISR-RL-DMPC • Cornerstone Project

## Slide 4
02 • Problem Statement
Formal Multi-Drone ISR Problem
Given N drones, maximize surveillance and target response while preserving safety and coordination.
Optimization objective (per drone i):
min Σ_{k=0}^{N-1} [ e_k^T Q_eff^(i) e_k + u_k^T R_eff^(i) u_k ] + e_N^T P e_N
Subject to: x_{k+1}=Ax_k+Bu_k, ||u_k||<=u_max, ||p_i-p_j||>=r_min, and mission constraints.
Need: 50 Hz operation, distributed scalability, and robust estimation under sensor noise.
ISR-RL-DMPC • Cornerstone Project

## Slide 5
03 • Methodology
System Architecture & Flow
Perception: Sensor fusion (EKF) + target state estimation
Decision: Mission planning + formation + classification + threat + task allocation
MARL: MAPPO outputs adaptive Q/R scale vectors (14-D action)
Consensus: ADMM synchronizes local DMPC sub-problems
Control: DMPC (CVXPY/OSQP) + geometric attitude controller (SO(3))
Analytics: Stability and performance diagnostics
ISR-RL-DMPC • Cornerstone Project

## Slide 6
Module Deep Dive 1: Drone State Space
DMPC state (11-D): x=[p_x,p_y,p_z,v_x,v_y,v_z,a_x,a_y,a_z,ψ,ψ̇]^T
Dynamics: x[k+1]=Ax[k]+Bu[k], with translational triple-integrator structure.
A embeds p←v and v←a coupling; B injects acceleration control into a-states.
Controllability theorem: translational (A_9,B_9) is fully controllable (rank 9).
Importance: provides stable, computationally tractable model for real-time QP.
ISR-RL-DMPC • Cornerstone Project

## Slide 7
Module Deep Dive 2: Extended Kalman Filter
Equations
Integration Role
Predict: x^- = f(x,u), P^- = FPF^T + Q
Update: K = P^-H^T(HP^-H^T+R)^(-1)
x = x^- + K(z - h(x^-)), P=(I-KH)P^-
Adaptive fusion: R_eff = R / confidence
Drone estimator: 18-D state assembly
Target estimator: 11-D tracking EKF per target
Fuses IMU, GPS, radar, optical, RF, acoustic cues
Provides reliable state feed for DMPC and decision modules
ISR-RL-DMPC • Cornerstone Project

## Slide 8
Module Deep Dive 3: Formation Consensus
Graph model G=(V,E), Laplacian L = D - A_adj governs convergence.
Consensus control term: u_consensus,i = k_c Σ_{j∈N(i)} (p_j - p_i).
Formation law combines position tracking, damping, and consensus coupling.
Convergence condition (discrete): Δt·k_c·λ_max(L) < 2.
Importance: maintains coherent geometry (line, wedge, grid, circular, sphere) across missions.
ISR-RL-DMPC • Cornerstone Project

## Slide 9
Module Deep Dive 4: Task Allocation (Hungarian)
Optimization Form
Cost Design
Linear Assignment Problem:
min_σ Σ_i C[i,σ(i)] subject to one-to-one assignment
Solved optimally in O(n^3) by Hungarian method.
Padding handles rectangular task/drone matrices.
C = 0.30 c_dist + 0.20 c_fuel + 0.20 c_load + 0.15 c_sensor - 0.15 priority
Infeasible assignments penalized with large cost.
Importance: aligns threat priorities with drone capabilities and endurance.
ISR-RL-DMPC • Cornerstone Project

## Slide 10
Module Deep Dive 5: DMPC Controller
Core QP solved each control cycle (50 Hz) via CVXPY + OSQP.
Terminal DARE equation defines P and LQR-consistent terminal penalty.
DARE: P = Q + A^TPA - A^TPB(R+B^TPB)^(-1)B^TPA
MAPPO adaptation: Q_eff = Q ⊙ diag(q_s), R_eff = R ⊙ diag(r_s), with scale clipping [0.1,10].
Importance: safety-constrained optimization with adaptive mission behavior.
ISR-RL-DMPC • Cornerstone Project

## Slide 11
Module Deep Dive 6: ADMM Consensus
Global consensus: minimize Σ_i f_i(z_i) subject to z_i = v for all i.
Augmented Lagrangian: L_ρ = Σ_i [f_i(z_i)+μ_i^T(z_i-v)+ (ρ/2)||z_i-v||^2].
Iterative steps per cycle: z-update (local), v-update (global average), dual update.
Residuals: primal r_prim and dual r_dual guide stopping criteria.
Theorem (Boyd et al.): for convex closed proper f_i, ADMM converges to optimum.
Integration role: aligns distributed plans without centralizing full trajectory optimization.
ISR-RL-DMPC • Cornerstone Project

## Slide 12
Module Deep Dive 7: MAPPO Agent
Learning Formulation
Interfaces to DMPC
CTDE: centralized critic V_φ(o^1,...,o^N), decentralized actor π_θ(o^i).
PPO clipping objective with entropy regularization.
GAE: Â_t = Σ_l (γλ)^l δ_{t+l}.
Obs: 40-D per drone, action: 14-D per drone.
Action = [q_scale(11), r_scale(3)]
These scales modulate DMPC weights online.
Preserves hard constraints while enabling policy adaptation.
Bridges learning with certifiable optimization layer.
ISR-RL-DMPC • Cornerstone Project

## Slide 13
Module Deep Dive 8: Geometric Attitude Control
Uses SO(3) formulation to avoid Euler-angle singularities (gimbal lock).
Attitude error: e_R = 0.5·vex(R_d^T R - R^T R_d).
Torque law: τ = -K_p,att e_R - K_d,att e_ω + ω×(Jω).
Motor mixing maps [F,τ_x,τ_y,τ_z] to [T1,T2,T3,T4] for X-quad geometry.
Importance: stable inner-loop realization of outer-loop DMPC accelerations.
ISR-RL-DMPC • Cornerstone Project

## Slide 14
Module Deep Dive 9: Stability, ISS, and CBF
Lyapunov candidate: V(e)=e^T P e, with P from DARE (positive definite).
For LQR closed loop: ΔV = -e^T(Q + K^TRK)e < 0 ⇒ asymptotic stability.
ISS bound quantifies disturbance-to-state gain under bounded perturbations.
CBF safety function: h_ij = ||p_i-p_j||^2 - r_min^2; enforce forward invariance.
Recursive feasibility discussed with terminal-set assumptions and implementation caveats.
ISR-RL-DMPC • Cornerstone Project

## Slide 15
Integrated Methodology Flow
Sensors → EKF fusion → classification/threat assessment → task allocation
Mission planner + formation controller define references and geometry constraints
MAPPO outputs adaptive Q/R scales per drone each step
ADMM drives local DMPC plans to consensus
DMPC computes constrained optimal accelerations
SO(3) attitude controller converts commands to motor thrusts in physics simulator
ISR-RL-DMPC • Cornerstone Project

## Slide 16
04 • Challenges
Key Challenges and How We Addressed Them
1) Non-convex collision constraints vs QP solver requirements (handled with practical approximations/CBF framing).
2) Stability guarantees under online MARL scaling of Q and R.
3) Maintaining 50 Hz timing with distributed optimization overhead.
4) Partial observability and asynchronous multi-sensor measurements.
5) Swarm-scale communication and consensus robustness under delays/dropouts.
ISR-RL-DMPC • Cornerstone Project

## Slide 17
05 • Results & Analysis
Results and Analytical Validation
Observed System Behavior
Quantitative Indicators
• Stable trajectory tracking across scenarios
• Coherent formation maintenance with ADMM coupling
• Real-time feasible optimization loop
• Robust estimation and mission-level responsiveness
• Spectral radius ρ(A_cl) ≈ 0.983 (<1)
• ADMM residuals converge within 3–5 iterations
• Stability report: Lyapunov/Eigenvalue/ISS/CBF checks pass
• Comparative analysis notebook available for DMPC vs RL-adaptive DMPC
ISR-RL-DMPC • Cornerstone Project

## Slide 18
06 • Novelty
Novel Contributions
• MARL policy adapts MPC cost weights online instead of replacing MPC safety core.
• ADMM-based consensus integrated directly with per-agent DMPC and mission modules.
• Full-stack ISR pipeline: sensing, estimation, planning, allocation, control, and analytics.
• CTDE MAPPO design tailored to swarm coordination under partial observability.
• Practical bridge between theoretical control guarantees and adaptive learning behavior.
ISR-RL-DMPC • Cornerstone Project

## Slide 19
07 • Conclusion
Conclusion
Takeaways
Future Work
• Delivered a modular ISR swarm framework with adaptive DMPC.
• Demonstrated mathematically grounded control plus RL adaptation.
• Achieved integrated end-to-end mission flow in simulation.
• Provided reproducible architecture, docs, and analysis.
• Explicit terminal set constraints for stronger guarantees
• Improved convex-safe collision formulations
• Hardware deployment and HIL validation
• Larger swarm scaling with communication constraints
ISR-RL-DMPC • Cornerstone Project

## Slide 20
Thank You
Questions?
Repository: https://github.com/Cornerstone-swarm-drones/isr-rl-dmpc
Presentation includes methodology, module equations, analysis, and conclusions.
ISR-RL-DMPC • Cornerstone Project